## Slide 1: EL 653
Synthesis and Optimization
Extracted from “Synthesis and Optimization of Digital Circuits”, Giovanni de Micheli,
McGraw-Hill, 1994

## Slide 2: Introduction
Synthesis techniques speed up the design cycle and reduce the human effort
Optimization techniques enhances the design quality
Synthesis and optimization are used in mostly all circuit design today

## Slide 3: IC Design
Front End
Architecture
Functional
Verification
RTL Design/Logic
Synthesis
Physical Design
Design
Integrity
process begin
wait until not
CLOCK'stable
and CLOCK=1;
if(ENABLE='1') then
TOGGLE<= not
TOGGLE;
end if;
end process;
Back End
Fabrication

## Slide 4: Circuit Models
Model is an abstraction, i.e. a representation showing relevant features without details
Synthesis is the generation of a circuit model starting from a less detailed one
Classification
  Levels of abstraction
  Views

## Slide 5: Levels of Abstraction
Architectural – the circuit performs a set of operations (HDL models or flow diagrams)
Logic – A digital circuit evaluates a set of logic functions (state transition diagrams or schematics)
Geometrical – a circuit is a set of geometrical entities (floor plans or layout)

## Slide 6: Views
Behavioral – describes the function of the circuit regardless of its implementation
Structural – describes a model as an interconnection of components
Physical – relates to the physical objects of a design (e.g. transistors)

## Slide 7: Levels of Abstraction and Views
architectural level
logic level
geometrical level
behavioral view
structural view
physical view
Gajski and Kun’s Y – chart

## Slide 8: Synthesis
Synthesis can be seen as a set of transformations between two axial views
Architectural level synthesis - generates a structural view of an architectural level model
Logic level synthesis – generates a structural view of a logic level model
Geometrical level synthesis – generates a physical view at the geometric level

## Slide 9: Architectural Synthesis
Behavioral level model represents a set of operations and dependencies
The architectural
  identifies the hardware resources that can implement the operations
  schedules the execution time of the operations
  binds the operations to the resources
Defines a structural model of a datapath (interconnection of resources) and a logic level model of the control unit (issues control signals to the datapath according the schedule)
Circuit area and performance depend on this synthesis

## Slide 10: Example
Let consider the differential equation in the interval [0,a] with step size dx and initial values x(0) = x, y(0) = y and y’(0) = u
We use the Forward Euler Method (numerical solution)
Circuit area and performance depend on this synthesis

## Slide 11
diffeq {
read (x,y,u,dx,a);
repeat {
x1 = x + dx
u1 = u – (3 * x * u * dx) – (3 *y * dx);
y1 = y + u * dx;
c = x1 < a;
} until (c)
write (y)
MULT
ALU
STEERING & MEMORY
CONTROL UNIT
Structural view
Structural HDL

## Slide 12: Logic Synthesis
Logic level model is provided by a state transition diagram or a finite state machine (FSM), or a circuit schematic (HDL model as well)
Can be specified by a designer or synthesized from an architectural level model
Logic synthesis is different depending on the nature of the circuit (sequential, combinational) and the type of the starting representation (state diagram or schematic)
Final outcome is a fully structural representation (e.g. netlist)

## Slide 13: Physical Design
Consists of generating the layout of the chip
Layers of the layout correspond to the masks used for fabrication
Depends on the design style (handcrafted or automatic)
Major tasks are placement and routing

## Slide 14: Optimization
Performed in general in conjunction with synthesis
Two optimization measures
  Area
  Performance

## Slide 15: Circuit Area
Extensive quantity
Correspond to the sum of the areas of the circuit components
Can be derived from a structural view of the circuit, once the area of each component is known
Area computation can be performed hierarchically
Wiring area plays an important role, can be derived from physical view or estimated from a structural view

## Slide 16: Circuit Performance
Intensive quantity, it is not additive
Computation requires a full analysis of the structure and the behavior of the circuit
Performance of a combinational circuit depends on the input/output propagation delay assuming all inputs are available at the same time
Performance of a synchronous sequential circuit is measured by its cycle time (looking for the fastest clock)
Circuit latency is the necessary time to execute the operations of the circuit. It could be measured in terms of clock cycles
Overall execution time is provided by the product between cycle time and latency
Cycle time and latency are optimized independently

## Slide 17: Circuit Performance
A synchronous circuit can implement a sequence of operations in a pipeline
The throughput of the circuit is the rate at which data are produced and consumed
In a non pipelined circuit, the throughput is less or equal than the inverse of the product of the cycle time and the latency
Maximum rate pipelining is when the throughput is the inverse of the cycle time (data are produced and consumed at each clock cycle)
Performance optimization
  Minimizes delay (combinational circuits)
  Minimizes cycle time and latency (synchronous circuits)
  Maximizes throughput (pipelined circuits)

## Slide 18: Design Optimization
Combines area minimization and performance maximization
Optimization is subject to constraints (upper bounds of the area and lower bounds of the performance)
Design space of a circuit – different feasible structural implementations
Design space is a finite set of design points
For each design point there are values of area and performance evaluation functions
There are as many evaluation functions as design objectives (area, latency, cycle time, and throughput)
Design evaluation space – multidimensional space of these objectives

## Slide 19: Design Optimization
Circuit optimization – a circuit design that optimizes all objectives
Assumes that the optimization problem is a minimization problem (maximizes the throughput is equivalent to minimize the complement of the throughput)
Pareto point – a point in the design space with no other point with at least an inferior objective
Pareto point – corresponds to a global optimum in a monodimensional design evaluation space
Set of the optimal trade-off points – image of the Pareto points in the design evaluation space
Trade-off curve or surface – interpolation of the set of the optimal trade – off points

## Slide 20: Combinational Logic Circuits
Objective design evaluation space (area – delay)
Trade-off points shown in figure
10
20
30
40
50
475
500
525
550
delay
area

## Slide 21: Sequential Logic Circuits
Design evaluation space for logic level models of sequential circuits is (area, cycle-time)
Design evaluation space for non pipelined architectural level model is (area, latency, cycle-time)
Design evaluation space for synchronous pipelined architectural level model is (area, latency, cycle-time, throughput)

## Slide 22: Optimization Approaches
Combinational logic circuits
  Minimize the circuit area under delay constraints
  Minimize the circuit delay under area constraints
Synchronous circuits
  Minimize the circuit area under latency constraints
  Minimize the circuit latency under area constraints

## Slide 23
Behavioral views
Language Models
Structural views
Abstract Models
HDL
HDL
HDL
Operations & dependencies
(Data flow & sequencing graphics
Architectural level
Logic level
compilation
FSMs – logic functions
(State diagrams & logic networks)
compilation
Architectural synthesis
& optimization
Interconnected logic blocks
(Logic networks)
translation
Logic synthesis
& optimization