## Slide 1: EL 653
Hardware Modeling
Extracted from “Synthesis and Optimization of Digital Circuits”, Giovanni de Micheli,
McGraw-Hill, 1994

## Slide 2: Introduction
A circuit model is an abstraction – a representation that shows relevant features without showing the details
Models are used
  Specify circuits
  Consider circuit properties
  Transfer information among humans and CAD tools
Circuit specifications: models describing a circuit to be implemented accompanied by constraints (area, performance)

## Slide 3: Models
Formal models
  Well defined syntax and semantics
  Conveys information that can be unambiguously interpreted
  Application for CAD tools
Informal models
  Textual description of the operation
  Limited application for CAD tools
  Produces misunderstanding among humans

## Slide 4: Models
A circuit can be modeled differently according to
  Abstraction level
    architectural
    logic
    geometric
  View
    behavioral
    structural
    physical
  Modeling means
    language
    diagram
    mathematical model

## Slide 5: Hardware Modeling Languages – HDL
Motivated by the need of specifying circuits
Fairly different from software programming languages
Hardware circuits can execute operations with a wide degree of concurrence. Software programs are commonly executed on uni-processors and operations are serialized
Specifications of hardware circuits entail structural information
Detailed timing of the operation is very important in hardware. Specific execution time frames of the operations in software programs are of less concern (except real time systems)

## Slide 6: Hardware Modeling Languages – HDL
HDLs use behavioral and/or structural views when describing architectural and logic level
Synthesis tools support the transformation of behavioral models into structural ones at the architectural and logic levels
HDLs have multiple purposes: specification, simulation, synthesis, etc.

## Slide 7: Features of Hardware Languages
A language is characterized by its syntax, semantic and pragmatic
Syntax relates to the language structure and is specified by a grammar
Semantic relates to the meaning of the language
Pragmatic relates to the other aspects of the language (e.g. implementation issues)

## Slide 8: Features of Hardware Languages
Languages can be classified as procedural and declarative
Procedural programs specify the desired action by describing a sequence of steps whose order of execution matters
Declarative programs express the problem to be solved by a set of declarations without detailing a solution method. Order of statements is not important

## Slide 9: Structural Hardware Languages
Describes an interconnection of components
“Similar” to circuit schematics
Hierarchy is used to make modular and compact descriptions
Variables correspond to port of components

## Slide 10: Behavioral Hardware Languages
Considered for more complex circuits
Combinational logic can be described by a set of ports (I/O) and a set of equations that relate variables to logic expressions
Declarative paradigm applied best to combinational circuits
Different paradigms have been used for sequential circuits
  set of assignment expressions
  procedural models where a variable keeps the state information (FSM)

## Slide 11: Abstract Models
Used to represent different circuit view at the logic and architectural levels
Based on graphs
Types
  structures
  logic networks
  state diagrams
  data-flow and sequencing graphics

## Slide 12: Compilation and Behavioral Optimization
Hardware compilation is analogue to software compilation
Software compiler
  Front end: transforms a program into an intermediate form
  Optimizer: Optimizes the intermediate form
  Back end: translates the intermediate form into the machine code for a given architecture
  Front end is language dependant and back end is machine dependent
Hardware compiler
  Front end
  Optimizer
  Back end

## Slide 13: SW and HW Compilers
lex
parse
optimization
codegen
front end
intermediate form
back end
lex
parse
behavioral
optimization
front end
intermediate form
back end
synthesis
synthesis
synthesis
Software Compiler
Hardware Compiler

## Slide 14: Compilation Techniques
The front end is responsible for lexical and syntax analysis, parsing and creation of the intermediate form
Lexical analyzer: component that read the source model and produces tokens that the parser uses for syntax analysis
The parser receives a set of tokens
  Verifies syntax rules satisfaction
  Generates a set of parse trees (tree-like representation of the syntactic structure of a language
  Syntactic and semantic errors are detected

## Slide 15: Example: a = p+q*r
assignment
=
expression
+
expression
*
identifier
r
identifier
a
identifier
p
identifier
q

## Slide 16: Optimization Techniques
Behavioral optimization is a set of semantic-preserving transformations that minimize the amount of information needed to specify the partial order of tasks
No knowledge about the circuit implementation style is needed
Can be implemented in different ways
  directly to parse trees
  during the generation of the intermediate form
  in the intermediate form itself

## Slide 17: Optimization Techniques
Data-flow-based transformations
  tree-height reduction
  constant and variable propagation
  Common subexpression elimination
  dead code elimination
  operator strength reduction
  code motion
Control-flow-based transformations
  model expansion
  conditional expansion
  loop expansion

## Slide 18: Tree-height Reduction
Applies to arithmetic expressions trees and strives to achieve the expression into two-operands expressions, so hardware parallelism can be used
Used mainly in local transformations because the limited parallelism
Exploits some arithmetic operations to balance the tree (commutative, associative, distributive

## Slide 19: Constant and Variable Propagation
Constant propagation detects constant operand and pre-computes the value of the operation with the operand. Can be made recursively
Variable propagation detects the copy of variables, and uses the right hand side in the following references in place of the left hand side

## Slide 20: Common Subexpression Elimination
The search for common arithmetic subexpressions looks for isomorphic patterns in the parse trees
Simplified if the arithmetic expressions are reduced to two inputs expressions

## Slide 21: Dead Code Elimination
Consists of all of those operations that cannot be reached, or whose result is never referenced elsewhere
Such operations are detected by data flow analysis and removed

## Slide 22: Operator Strength Reduction
Reduces the cost of implementing an operator by using a simpler one
For example a multiplication by 2 can be replaced by a shift

## Slide 23: Code Motion
Applies to loop invariants
Avoid repetitive evaluation of the same expression
If a and b are not updated into the loop

## Slide 24: Model Expansion
Consists in flattening locally the model call hierarchy
The scope of application of some optimization techniques is enlarged
If the expanded model is called only once, there is no counterpart. If it is called several times, it can increase the size of the intermediate code and the loss of the possibility of hardware sharing

## Slide 25: Conditional Expansion
Can be transformed into a parallel construct with a test in the end
This transformation can increase the performance of the circuit (conditional clause depends on late-arriving signals

## Slide 26: Loop Expansion
Applies to an iterative construct with data-independent exit condition
Loop is replaced by as many instances of its body as the number of operations
Benefit is expanding the scope of other operations